## Slide 1: Virtual Memory
Virtual memory, Translation lookaside buffer(tlb),demand paging, Thrashing, page replacement algorithm, working set model

## Slide 2: Introduction to Virtual Memory
Definition: Virtual memory enables a system to use more memory than physically available by using disk space as an extension of RAM.
Benefits:
  Supports multitasking and large applications.
  Provides process isolation.
  Simplifies programming by abstracting physical memory.
Concepts:
  Address space separation: Virtual vs. Physical.
  Enables efficient use of memory resources.

## Slide 3: Virtual Memory

## Slide 4: Virtual memory

## Slide 5: Translation Lookaside Buffer (TLB):
Definition: A small, high-speed cache that stores recent translations of virtual memory addresses to physical addresses.
Functionality:
  Reduces the time taken to access the page table for address translation.
  Avoids repeated memory lookups for frequently accessed pages.
Structure:
  Associative memory structure for quick matching.
Advantages:
  Improves performance significantly in systems with frequent memory access.
  Reduces latency associated with page table lookups.
Limitations:
  Limited size: Can only store a small number of entries.
  TLB misses require a fallback to the page table, incurring additional latency.

## Slide 6: Translation Lookaside Buffer (TLB):

## Slide 7: Demand Paging:
Definition: A technique where pages are loaded into memory only when they are needed, rather than preloading all pages of a process.
How It Works:
  When a process accesses a page not currently in memory, a page fault occurs.
  The operating system retrieves the page from disk and loads it into memory.
Advantages:
  Saves memory by loading only necessary pages.
  Reduces initial load time for processes.
Disadvantages:
  Page faults can slow down execution.
  Overhead from frequent disk access if too many page faults occur.
Example:
  Process needs pages A, B, C, D.
  Pages A and B are loaded initially.
  When the process accesses C, a page fault occurs, and C is loaded from disk.

## Slide 8: Thrashing:
Excessive paging activity causing performance degradation.
Mitigated by adjusting working sets.

## Slide 9: The Working Set Model
Definition:
  The working set of a process is the set of pages it has referenced within a recent time window (∆).
Key Concepts:
  Window Size (∆): Determines the recent time period to track references.
  Working Set Size (WSS): Number of pages in the working set.
  Dynamic Behavior: Adjusts as processes access different pages.
Applications:
  Prevents thrashing by ensuring processes have enough pages.
  Helps OS allocate memory efficiently.
Example:
  Process accesses pages: 1, 2, 3, 4, 1, 2, 5, 1, 2, 3, 4, 5.
  With ∆ = 4, the working set changes dynamically:
    After referencing page 5: {2, 3, 4, 5}.

## Slide 10: Page Replacement Algorithms First-In-First-Out (FIFO):
Replaces the oldest page in memory that was loaded first.
Advantages:
  Simple to implement.
Disadvantages:
  May replace frequently used pages, leading to high page faults.
Example:
  Reference string: 7, 0, 1, 2, 0, 3, 0, 4, 2, 3, 0, 3, 2
  Frames: 3
  Total Page Faults: 9

## Slide 11: Least Recently Used (LRU):
Replaces the page that has not been used for the longest time.
Advantages:
  Reduces page faults by considering usage patterns.
Disadvantages:
  Overhead to track recent usage.
Example:
  Reference string: 7, 0, 1, 2, 0, 3, 0, 4, 2, 3, 0, 3, 2
  Frames: 3
  Total Page Faults: 10

## Slide 12: Optimal Page Replacement:
Replaces the page that will not be used for the longest time in the future.
Advantages:
  Minimal page faults (theoretical best).
Disadvantages:
  Requires future knowledge of reference string.
Example:
  Reference string: 7, 0, 1, 2, 0, 3, 0, 4, 2, 3, 0, 3, 2
  Frames: 3
  Total Page Faults: 7

## Slide 13: Most Recently Used (MRU):
Replaces the most recently used page.
Advantages:
  Useful when recently used pages are less likely to be reused.
Disadvantages:
  Poor performance in certain scenarios.
Example:
  Reference string: 7, 0, 1, 2, 0, 3, 0, 4, 2, 3, 0, 3, 2
  Frames: 3
  Total Page Faults: 10